## Slide 1: Course: Embedded System Design and Modeling Topic: Finite State Machine
Class at Lewis University
Yue Cao Purdue University, ECE yuecao@purdue.edu

## Slide 2: Resources
Second Edition, 2017
eBook online
2009
Supporting slides online
Fifth Edition, 2022
Supporting slides online
system level design
general topics, hardware & software

## Slide 3
What is an Embedded System?

## Slide 4: What is an Embedded System?
any device that includes a programmable computer, but is not itself intended to be a general-purpose computer
less visible computers
application specific
and tightly constrained by different requirements

## Slide 5
Are they embedded systems?

## Slide 6
Are they embedded systems?

## Slide 7
Design Philosophy
Hardware/Software CoDesign
display
memory
processor
GPS receiver
panel I/O
user interface
database search
route planning
rendering
software
hardware

## Slide 8
A Topic in Software Design
How do we organize multiple events in code?

## Slide 9
A Topic in Software Design
How do we organize multiple events in code?
One Solution for All: Finite State Machine

## Slide 10: Finite State Machine
Start with a basic example
are signals,
are ports

## Slide 11: Finite State Machine
Represent it in “States”
are signals,
are ports
If we have M parking spots,
then the display need to show {0, 1, 2, … ,M}.
We call {0, 1, 2, … ,M} as the states of the system.

## Slide 12: Finite State Machine
Represent it in “States”
are signals,
are ports
If we have M parking spots,
then the display need to show {0, 1, 2, … ,M}.
We call {0, 1, 2, … ,M} as the states of the system.
Draw in a graph:
System transits from one state to another. At each time step, one car arrivals or departs, or both happen, or neither happen

## Slide 13: Finite State Machine

## Slide 14: Finite State Machine
Configure Transitions
We know what are the “States” now.
Then what about these transition lines?

## Slide 15: Finite State Machine
Configure Transitions
We know what are the “States” now.
Then what about these transition lines?
as an example: is transition condition, or called guard. 1 is the output, or called action, means display changes to 1.

## Slide 16: Finite State Machine
Let’s see another example
States? Guard? Action?
60
80

## Slide 17: Finite State Machine
Let’s see another example
States: {cooling, heating} Guard? Action?
60
80

## Slide 18: Finite State Machine
Let’s see another example
States: {cooling, heating} Guard: Action:
60
80

## Slide 19: Finite State Machine
We just used graphs to organize events and their transitions.
They are examples of Finite State Machine
Definition
  state machine a model of a system with discrete dynamics that at each reaction maps valuations of the inputs to valuations of the outputs, where the map may depend on its current state
  finite state machine a state machine where the set States of possible states is finite.

## Slide 20: Finite State Machine
We just used graphs to organize events and their transitions.
They are examples of Finite State Machine
Definition
  state machine a model of a system with discrete dynamics that at each reaction maps valuations of the inputs to valuations of the outputs, where the map may depend on its current state
  finite state machine a state machine where the set States of possible states is finite.

## Slide 21: Finite State Machine
We just used graphs to organize events and their transitions.
They are examples of Finite State Machine
Definition
  state machine a model of a system with discrete dynamics that at each reaction maps valuations of the inputs to valuations of the outputs, where the map may depend on its current state
  finite state machine a state machine where the set States of possible states is finite.

## Slide 22: Finite State Machine
Visual notation for a finite state machine
Note: 1. transition condition, or called guard, or called input 2. output, or called action

## Slide 23: Finite State Machine
Add-on: Mealy Machines and Moore Machines
Some Reddit comments

## Slide 24: Finite State Machine
Add-on: Mealy Machines and Moore Machines
  George H. Mealy’s paper in 1955: “A method for synthesizing sequential circuits ”
  Edward F. Moore’s paper is 1956: “Gedanken-experiments on sequential machines”

## Slide 25: Finite State Machine
Add-on: Mealy Machines and Moore Machines
  Mealy Machines: produce output when a transition is taken.
  Moore Machines: produce output when the system is in a state.
Note: regular M is the state, italic M is the output.
Note: We will stay with Mealy machines in this class

## Slide 26: Finite State Machine
Add-on: Mealy Machines and Moore Machines
b
button: 0 1
light: a b
Example: 2 light, 2 button system press any button continuously, light b flashes; press any button once but not the previous situation, light a flashes.
-Press: 0 1 1 0 1 0 0 0
-Flash: a a b a a a b b

## Slide 27: Finite State Machine
Add-on: Mealy Machines and Moore Machines
Example: 2 light, 2 button system press any button continuously, light b flashes; press any button once but not the previous situation, light a flashes.
-Press: 0 1 1 0 1 0 0 0
-Flash: a a b a a a b b
A
B
C
0/a
0/b
1/b
1/a
1/a
0/a
Mealy machine
button: 0 1
light: a b

## Slide 28: Finite State Machine
Add-on: Mealy Machines and Moore Machines
Example: 2 light, 2 button system press any button continuously, light b flashes; press any button once but not the previous situation, light a flashes.
-Press: 0 1 1 0 1 0 0 0
-Flash: a a b a a a b b
A
B
C
0/a
0/b
1/b
1/a
1/a
0/a
Mealy machine
0
A
/-
B
/a
C
/a
1
B’
/b
0
0
1
C’
/b
1
0
1
Moore machine
(typically need more states)
0
1
button: 0 1
light: a b

## Slide 29: Finite State Machine
How to program it in code?
Example: A special power supply, output different voltages over time
A
B
C
Clock=2s/Voltage=110V
Clock=9s/Voltage=220V
Clock=14s/Voltage=110V
Clock=20s/Voltage=0V

## Slide 30: Finite State Machine
Idea 1: Program transition by transition
A
B
C
Clock=2s/Voltage=110V
Clock=9s/Voltage=220V
Clock=14s/Voltage=110V
Clock=20s/Voltage=0V
Each transition as an “if-else” statement.
What if too many transitions?

## Slide 31: Finite State Machine
Idea 2: Program state by state
A
B
C
Clock=2s/Voltage=110V
Clock=9s/Voltage=220V
Clock=14s/Voltage=110V
Clock=20s/Voltage=0V
Still hard to read or modify?
Any neat way to code?

## Slide 32: Finite State Machine
Idea 3: Program by state transition table
A
B
C
Clock=2s/Voltage=110V
Clock=9s/Voltage=220V
Clock=14s/Voltage=110V
Clock=20s/Voltage=0V
Current State | Clock Condition | Next State | Output Voltage
STATE_A | 2 | STATE_B | 110
STATE_B | 9 | STATE_C | 220
STATE_C | 14 | STATE_B | 110
STATE_B | 20 | STATE_A | 0
Define a new structure
Everything is in this table

## Slide 33: Wrap-Up
Intro to embedded systems
Finite State Machine
  Definition
  Mealy and Moore
  Coding strategy